## Slide 1
Real-Time RCS Detection
The Product
Real-Time RCS Detection
Provide Real-time, instantaneous information on changing Silica levels in industrial environments
Provide on-device / control room display of RCS measurement in mg/m3
Rolling averaging periods based on 1min, 15min, 1hr, 4hrs, 8hr shift patterns
On device Warnings and Alarms based on custom trigger thresholds (0.05 mg/m3 for example)
Data logging for download and post analysis using the Trolex BreatheXS software application, exportable to CVS file

## Slide 2
Real-Time RCS Detection
The Method
Real-Time RCS Detection
Airflow Per Litre (Dynamic)
~10,000 triggers per second
Particle count per second
Particle Density
Positive RCS count over general dust
RCS content in mg/m3
From the sampled airflow the Air XS Sensor determines the following to support the identification of RCS particles
Sample Air Flow ~1.5L/min
Sample Exit Flow
Filtered Sheath Flow

## Slide 3
Real-Time RCS Detection
Real-Time RCS Detection
Sample Air Flow ~1.5L/min
Sample Exit Flow

## Slide 4
Real-Time RCS Detection
Optical Refraction Technology (ORT)
Real-Time RCS Detection
Laser Lightsource
Particulate Sizes 10um – 1um
Particle size, shape, symmetry and structure
Particulate Size
Signatures
Particulate Density
Light Absorption
Optical Wavelength
Optical Diffraction
Reference Density Bulk / Particle
Reference input vs. output for reference material types
Specifically tuned for Particle Types
Changes in optical Light Scatter / Diffraction Pattern

## Slide 5
Real-Time RCS Detection
Device Measurement
Real-Time RCS Detection
Sample Concentration
Total volume of Air (Litres) sampled over a given time
Silica Content
Volume of Silica Particles sampled from 1 – 10µm in counts and mg.m-3
Mixed Particulates
Volume of Particles sampled from 1 – 40µm in counts

## Slide 6
Real-Time RCS Detection
Active Sampling Area
Real-Time RCS Detection
Airborne particulates drawn into device relative to the dust inlet port situated on the top of the device.
Active sampling area typically draws from a ~1m radius in calm air conditions.
Devices should be positioned relative to particle generation sources or areas of interest
Sampling can be influenced by environmental conditions such as airflow, local extraction and ambient surroundings.
Sampling Zone

## Slide 7
Real-Time RCS Detection
Sensing Parameters
Real-Time RCS Detection
Max Dust Loading
150 mg/m3
Continuous Loading
25 mg/m3
L.O.D
1 µm (micron) Particulate
1 µg/m3 (Microgram) Mass

## Slide 8
Real-Time RCS Detection
Device Connectivity
Real-Time RCS Detection
USB Data Download
Windows / Mac PC
Or Network
Ethernet or RS485 Serial
(Data Registers)
AC or DC Power Input
Breathe XS Desktop Application

## Slide 9
Real-Time RCS Detection
Device Set-Up
Real-Time RCS Detection
AC Power
Fixed Location Monitoring
Transportable Monitoring
Data / Comms
DC Power
USB Data Download

## Slide 10
Real-Time RCS Detection
Device Power On and Sampling
Real-Time RCS Detection
1.
3.
2.
Start Up Splash Screen
Warm Up / Self Test
Sampling…

## Slide 11
Real-Time RCS Detection
On Device Display Readout
Real-Time RCS Detection
15 mins
mg.m-3
RCS
00.04
content
Particles /L
2350
Sampling Time

## Slide 12
Real-Time RCS Detection

## Slide 13
Real-Time RCS Detection
Key Installation Notes
Real-Time RCS Detection
Humidity may impact the aerodynamic size of some particles.
Device positioning should be considered relative to dust suppression systems or airborne mist or suppressants.
Device cleaning regimes may need to be considered depending on environmental dust loading.

## Slide 14
Real-Time RCS Detection
Key Installation Notes
Real-Time RCS Detection

## Slide 15
Real-Time RCS Detection
Device Testing and Benchmarking
Real-Time RCS Detection
Internal Lab Benchmarking
Site Stress Testing
Independent Verification

## Slide 16
Real-Time RCS Detection
Device Testing and Benchmarking
Real-Time RCS Detection
Internal Lab Benchmarking
Site Stress Testing
Independent Verification

## Slide 17
Real-Time RCS Detection
Device Testing and Benchmarking
Real-Time RCS Detection
Internal Lab Benchmarking
Site Stress Testing
Independent Verification

## Slide 18
Real-Time RCS Detection
Device Testing and Benchmarking
Real-Time RCS Detection
Internal Lab Benchmarking
Site Stress Testing
Independent Verification
Results-driven Soil Science professional with a diverse background spanning laboratory analysis, project management, and teaching. A proactive researcher dedicated to innovative solutions for environmental challenges, with a strong publication record in prestigious journals.