## Slide 1
Presented by: Booth Armstrong
AeroFit & Quantifit2 Respirator Fit Testing

## Slide 2: Why Do We Fit Test?
Protect the health of employees
Poor fit is the largest contributor to poor protection (Grinspun et al. 2009)
Ensures respiratory protection effectiveness.
Prevents workplace exposure to harmful airborne particles.
Builds confidence, morale, and safety culture among employees.
Compliance with OSHA and other safety regulations.

## Slide 3: Who Can Fit Test?
Competent Individual?
Qualified Individual?
Program Administrator?
Anyone?

## Slide 4: When to Fit Test?
As part of the initial respirator selection
Where an untested facepiece is already in use

## Slide 5: How About a Repeat Test?
When the wearer:
Loses or gains significant weight (+/- 20lbs or 9kg)
Undergoes any substantial dental work
Develops any facial changes (scars, moles, etc.) around the face seal area
At the regulated time interval (typically annually)

## Slide 6
CNP
  OHD QuantiFit2
  Air is the challenge agent
  Uses a Controlled Negative Pressure to directly measure respirator leakage
Ambient Aerosol CNC
  OHD AeroFit
  Aerosol is the challenge agent
  Calculates the ratio of external particles to the particles in the mask
OSHA 1910.134 Appendix A

## Slide 7: Condensation Nuclei Counting
Uses laser technology to measure aerosol concentrations inside and outside the respirator.
Respirator must be equipped with high efficiency filters.
The idea is that because few particles penetrate a high efficiency filter, any found inside the respirator can be attributed to face seal leakage.
Measures the concentration of particulates in the respirator while the test subject is performing a series of exercises.
The ratio of this concentration in the breathing zone to the ambient particulate concentration is the Fit Factor.

## Slide 8: CNC
Benefits:
Can fit test any tight-fitting respirator
Limitations
Environmental requirements
Consumables
Test subject should not eat or smoke for
30 minutes before testing
Key Advancement
Replacing qualitative testing methods when testing FFR/N95 respirators

## Slide 9: Controlled Negative Pressure
Uses Controlled Negative Pressure technology directly related to a scientifically validated modelled breathing rate to measure respirator leakage.
Respirator must be equipped with fit test adapters.
The idea is that once a controlled pressure is achieved within the respirator facepiece, any air that is removed is the result of leakage.
CNP precisely measures leak rate in cc/min after a series of exercises.
The ratio of this leak rate to the modelled breathing rate is the Fit Factor.

## Slide 10: CNP
Benefits:
No Environmental Requirements
Highly Portable
Battery Power
Limitations
Cannot fit test Filtering Facepiece Respirators
Key Advancement
The most efficient testing method for quantitatively testing respirators with elastomeric /rubber seals

## Slide 11: AeroFit & QuantiFit2 Product Demonstration
  User Interface
  Respirator Selection Process
  Inputting Test Subjects
  Record-Keeping Features
  Fit Test Reporting Capabilities: QuantiFit2, Logic PC Software, LogicCloud

## Slide 12: Additional Solutions
OHD LogicCloud:
  Automatic scheduling of employees withnotifications
  Centralized data
  Advanced reporting
OHD Pre-Paid Calibration Packages & Extend Warranties

## Slide 13
Thank you!